## Slide 1: Turkey Creek Restoration Feasibility Study Summary City of Palm Bay
April 20, 2023

## Slide 2: Turkey Creek Summary
City acquired a FDEP 319 Grant for $160,000 for Turkey Creek restoration feasibility study
Geosyntec and Applied Ecology performed a holistic approach to identify improvement opportunities

## Slide 3: Turkey Creek Summary
Specifically, the project examined
  Muck dredging
  Cadillac Island removal and Sump Maintenance
  Ecological restoration
  Benefits of mechanical harvesting vs herbicides
  Wastewater treatment systems
  Stormwater and baseflow

## Slide 4: Turkey Creek Summary: Dredging of Turkey Creek
Dredging under current authorization (>5 foot deep)
  Several areas under 5-foot deep with nutrient rich sediment
Removal of muck represents several benefits
  Improved flow conditions
  Reduced nutrient reservoir
  Restore safe navigational access
Limitations
  Will not reach natural substrate in areas, will continue/increase nutrient flux
  No BMAP credit for these areas
  Has not, by itself, provided long-term net benefit

## Slide 5: Turkey Creek Summary: Excavation and Dredging of Islands
Removal of Cadillac Island
  Improves flushing and local navigation
  Ecological net gain due to exotics dominance
Maintenance of sump
  Annual inspection and after major storm events

## Slide 6: Turkey Creek Summary: Ecological Restoration - Outlaw Island
Removal of Invasive Species and Restoration of Native Plants
  Priority Project: Outlaw Island Restoration
  Overgrown with Brazilian pepper, Chinese tallow, elephant ear, climbing hemp fern

## Slide 7: Turkey Creek Summary: Ecological Restoration - Goode Park Shoreline Enhancement
Shoreline enhancements
  Priority Project: Goode Park (650 linear feet)
  Installation of a swale landward of top of bank, create softer side slope and plant desirable vegetation)
  Largest immediate public benefit
  Enhancement proposed east of the limits of the public fishing pier to property line
  Reduce erosion and nutrient runoff
  Improve fishery habitat and aesthetics

## Slide 8: Turkey Creek Summary : Stormwater Pond Ecological Restoration – Chace Lane/Cadillac
Repair stormwater pond/ Also a WQ project!
  Weir discharging steadily into Turkey Creek
Remove Brazilian Peppers and replace with native vegetation
  Area west of stormwater pond (1.5 acres)
  Cadillac Drive wetland area
Improve wetland hydrology
  Redirect stormwater to wetland
  Additional treatment

## Slide 9: Turkey Creek Summary: Wastewater Improvement Project Identification
Summary of available wastewater information was reviewed
  Septic systems – number of projects identified in previous studies and proposed for SOIRL funding
  Wastewater infrastructure – recently upgraded selected older communities
  Water reclamation facilities –upgraded to reduce effluent, continuing to monitor impact
  Groundwater monitoring study (AEI) – identified areas of interest
Recommend building on previous efforts

## Slide 10: Turkey Creek Summary: Stormwater and Baseflow Nutrient Loading
Refined subbasins used to determine TN and TP loading
Performed Hotspot analysis based on subbasin TN and TP loading
Identified water quality improvement projects
  Develop concept
  Evaluate pollutant removal performance
  Perform cost benefit analysis
TN Hotspot Maps
TP Hotspot Maps

## Slide 11: Turkey Creek Summary: Stormwater and Baseflow Improvement Project – Cadillac Drive
Enhance and repair pond
  Project cost $927,868
  Removal of 95.2 lbs/yr TN & 15 lbs/yr TP
  Cost benefit
    $487 /lb TN
    $3,101 /lb TP

## Slide 12: Turkey Creek Summary: Stormwater and Baseflow Improvement Project – Robert J Conlan Blvd
Enhance pond and add wetland filter and pump
  Project cost $912,517
  Removal of 444.2 lbs/yr TN & 47.1 lbs/yr TP
  Cost benefit
    $103 /lb TN
    $970 /lb TP

## Slide 13: Turkey Creek Summary: Stormwater and Baseflow Improvement Project – Ladner Road NE
Add pump and containerized filtration system for baseflow treatment
  Project cost $556,993
  Removal of 56.7 lbs/yr TN & 11.6 lbs/yr TP
  Cost benefit
    $491 /lb TN
    $2,415 /lb TP

## Slide 14: Turkey Creek Summary: Potential Funding Sources
FDEP
  Clean Water State Revolving Fund
  FDEP 319(h) Grants (typically require 40% match)
  FDEP Water Quality Assistance Grants (no match)
  FDEP Wastewater Grant Program
  Resilient Florida Grants (Planning, Implementation, Supplemental; some have match)
  Division of Water Restoration Assistance (DWRA) – wastewater grant program
IRC/IRLNEP Program
  Water quality focused
SOIRL
  Funding through SOIRL Trust Fund (due annually the first week of October)
Florida Legislature
  Appropriations

## Slide 15: Turkey Creek Summary: Recommendations
Keep holistic approach to restoration
Invest in data collection
  Surface water sampling
  Stormwater sampling
  Sediment assessment
Implement priority ecological restoration projects
Perform sediment island removal and maintain sump
Perform in-creek sediment assessment and evaluate long-term dredging benefits

## Slide 16: Turkey Creek Summary: Recommendations
Transform aquatic vegetation management program from chemical treatment to mechanical harvesting
Implement septic to sanitary project recommended by Wade Trim (2017)
Implement recommended stormwater and baseflow projects
Perform water quality assessment of MTD Canal watershed and identify upstream projects

## Slide 17: Questions??